## Slide 1: STM32 vs GD32 middleware benchmark
Comparative evaluation of middleware efficiency on Cortex- platforms
DKHILI Fares

## Slide 2: Presentation plan
Defined the benchmark scope, KPIs, and comparison methodology.
Introduction
USB Stack
FreeRTOS
FatFs
01
Benchmarked HID, CDC across footprint, timing, and transfer metrics.
02
Compared normalized native FreeRTOS scenarios on STM32 and GD32.
03
Developed custom tools for map analysis, cross-vendor comparison, and AI-assisted support.
04
Conclusion
Summarized results and continuation plan
06
Personal Contributions

## Slide 3: Introduction General Benchmark Overview
Objective
Workflow Process
Stages
Teams outline short-term goals and deliverables for the defined duration.
Create benchmark Scenarios and build them for both vendors.
Plan
Build
01
02
Extract KPIs from projects (footprint, performance etc..)
Extract
03
Data analysis and interpretation and enhancement proposals.
Final output is released to marketing team for immediate feedback and use.
Interpret
Deliver
01
02
❑ Develop similar scenarios on ST and peer MCU platforms using their embedded software frameworks of the scenarios across different platforms.
❑ Conduct functional testing to assess performance, memory footprint and robustness
❑ Compile a comprehensive benchmark report summarizing the results, insights, and recommendations for ST framework improvements

## Slide 4: Introduction Previously done benchmarks and marketing team review

## Slide 5: Introduction Benchmarks plan and done work

## Slide 6: Introduction Benchmarks plan and done work

## Slide 7: Introduction
Benchmarking middleware behavior across STMicroelectronics and Giga Device
USB Stack
CDC
MSC
HID
FreeRTOS
Cooperative test
Preemptive test
Basic processing test
FileSystem
Initial Scope
Footprint
Initialization / Bring-up Time
Latency
Throughput
Comparison Focus
Benchmark Support Tooling
Custom tools were developed to automate map-file analysis, compare cross-vendor footprint deltas, and support AI-assisted scenario porting, build, debug, and result interpretation.
USB Stack
FreeRTOS
FileSystem
Footprint

## Slide 8: ST Competitors MW Benchmark: USB Stack ST vs GD32
USB Benchmarking Scope
This section presents the USB Device benchmarking work performed across the three selected standard classes: HID, CDC, and MSC. The objective was to compare the middleware behavior of STM32 and GigaDevice implementations under equivalent application scenarios, while focusing on the most relevant USB performance indicators.
The comparison emphasized code footprint, initialization and enumeration behavior, communication latency, and transfer performance. In addition to class-level scenarios, particular attention was given to descriptor handling, host interaction, and class-specific transfer semantics, since these factors directly affect fairness and result interpretation.
The following slides detail the benchmark methodology, the implemented scenarios, and the observations collected for each USB class.

## Slide 9: ST Competitors MW Benchmark: USB ST vs GD32 Flowcharts
BareMetal mode : ST/GD USB Library USB HID device class
STM32U575xx (CM33) vs GD32E507(CM33)
BareMetal mode : ST/GD USB Library CDC device class
STM32U575xx (CM33) vs GD32E507(CM33)
USB Device Init
Clock configuration
Is device inserted ?
USB enemeration
Send mouse report
Start
Yes
No
Clock source : HSI (ST) / FIRC_48M (NXP)
Clock frequency: CM33: 160 MHz (ST and GD)
U5/ GD32: USB Full Speed, USB Device, CDC class
USB host (PC) identify, assign address and configure USB device (MCU)
USB HID device class: USB Human Interface Device allows to enable communication between device (MCU) and host (PC).
Yes
No
Yes
No
Clock configuration
USB configuration
If USB Receive data
USB transmit data
Is device inserted ?
Start
USB enemeration
Clock source : HSI (ST) / FIRC_48M (NXP)
Clock frequency: CM33: 160 MHz (ST and GD)
U5/ GD32: USB Full Speed, USB Device, CDC class
USB host (PC) identify, assign address and configure USB device (MCU)
USB CDC device class: USB communication device class allows devices to communicate with computers as serial ports or network interfaces.

## Slide 10: ST Competitors MW Benchmark: USB ST vs GD32 Flowcharts
BareMetal mode : ST/NXP USB Library HID device class
BareMetal mode : ST/NXP USB Library CDC device class
Execution time (ms)
 | STM32U575xx | MCX-N94X | ST vs NXP | Comment
ROM | 17013 | 13549 | +25.5% | * STM32 RCC Clock config 4560 bytes * FSL clock config 1470 bytes
RAM | 3065 | 1 360 | +125% | 
Total | 20078 | 14909 | +34% | 
Footprint (Bytes)
Execution time (ms)
Footprint (Bytes)
 | STM32U575xx | MCX-N94X | ST vs NXP | Comment
Initialize | 10 | 5 | +100% | 
Enumeration | 319.1 | 321.1 | -1% | 
Data transmission | 0.0092 | 0.00921 | 0% | 
 | STM32U575xx | MCX-N94X | ST vs NXP | Comment
ROM | 16377 | 13728 | +19.30% | * STM32 RCC Clock config 4560 bytes * FSL clock config 1558 bytes
RAM | 2422 | 1702 | +42.30% | 
Total | 18 799 | 15430 | +21% | 
STM32U575xx (CM33) vs MCX-N9 XX (CM33): : USB FS/ With RCC
STM32U575xx (CM33) vs MCX-N94 XX (CM33): USB FS
STM32U575xx (CM33) vs GD32E507(CM33): USB FS
STM32U575xx (CM33) vs MCX-N94X (CM33): USB FS/ With RCC
 | STM32U575xx | MCX-N94X | ST vs NXP | Comment
Initialize | 9,993 | 8,159 | +22% | 
Enumeration | 72 | 70.4 | +2% | 
Transmit data | 0.00945 | 0.0095 | -1% | 
Receive data | 0.0094 | 0.0094 | 0% | 
 | STM32U575xx | MCX-N94X | ST vs NXP | Comment
ROM | 12453 | 12087 | +3% | By removing clock configuration footprint, ST is higher by only 15% than NXP instead of 34%
RAM | 3065 | 1352 | +126% | 
Total | 15518 | 13439 | +15% | 
STM32U575xx (CM33) vs MCX-N94X (CM33): USB FS/ Without RCC
 | STM32U575xx | MCX-N94X | ST vs NXP | Comment
ROM | 11817 | 12282 | -3.79% | By removing clock configuration footprint, ST is higher by only 2.6% than NXP instead of 21%
RAM | 2422 | 1590 | +52% | 
Total | 14239 | 13872 | +2.6% | 
STM32U575xx (CM33) vs MCX-N9 XX (CM33): : USB FS/ Without RCC

## Slide 11: Section title

## Slide 12: ST Competitors MW Benchmark: RTOS Flowcharts
Clock frequency: 160 MHz
Start
Clock configuration
LOW Priority
Create Counting Thread
Create Reporting Thread
Start the scheduler
Initialize a global counter to 0
1 ms time slice/task
Start Counting Thread
Initialize an array to 0
Update array elements
Increment the global counter
Start Reporting Thread
Initialize last_counter to 0
Sleep for 30 s
Print :global counter – last counter
HIGH Priority
counter holding previous
Counter value
Thread blocked for 30s and only
Thread0 runs and loop back again
To sleep for 30s
Basic Processing Flowchart
HIGH Priority
Clock configuration
Create 5 threads
Create Reporting Thread
Start the scheduler
Initialize 5 global counters to 0
Start Thread i
Task Yield
Increment Ci
Start
Start Thread i+1
Task Yield
Increment Ci+1
i+1 = 4
i+1 = 4
Clock frequency: 160 MHz
c0 to c4
same low priority
1 ms time slice/task
Cooperative Processing Flowchart
Start Reporting Thread
Sleep for 30 s
Print the 5 counters
HIGH Priority
Clock configuration
Create 5 threads
Create Reporting Thread
Suspend thread 1,2,3,4
Initialize 5 global counters to 0
Start Thread i
Resume thread i
Increment Ci
Start
Start Thread i+1
Resume thread i+1
Increment Ci+1
To Next thread
From Next thread
Clock frequency: 160 MHz
c0 to c4
ascending priorities ,from lowest to highest
Suspend Threads 1 through 4 ;start with Thread 0 active
Suspend Ci+1
Preemptive Scheduling Flowchart
Start Reporting Thread
Sleep for 30 s
Print the 5 counters

## Slide 13: IAR EWARM Map File Analyzer
From raw linker map files to benchmark-ready memory reports

## Slide 14: MCU workflow studio The problem we solve
Current challenge
IAR map files are rich in data but hard to exploit quickly
Manual analysis is slow and error-prone
Technical benchmark evidence is not always presentation-ready
Comparing STM32 vs competitors takes too much engineering effort
Impact
Delays benchmark creation
Inconsistent reporting across teams
Harder to build convincing memory-footprint narratives
Key message:
transforming complex linker output into clear, reusable benchmark evidence.

## Slide 15: IAR EWARM Map File Analyzer Solution overview
MCU Workflow Studio solves this
Deterministic firmware comparisonCross-vendor analysis (STM32, NXP, TI, etc.)Converts raw map files → actionable insights
✅ Output:MappingsMetricsRecommendations

## Slide 16: IAR EWARM Map File Analyzer key features
Deterministic scoring engine
Layer-based analysis
Cardinality detection
Recommendation engine
Optional AI enhancement

## Slide 17: IAR EWARM Map File Analyzer System Overview
Inputs: .map / .xlsx
Processing: parsing, scoring, analysis
Outputs: reports, mappings, recommendations

## Slide 18: IAR EWARM Map File Analyzer End-to-end workflow
Workflow
User launches the desktop application
User selects an IAR .map file
Tool parses the file and identifies key sections
Tool computes memory KPIs
User explores results in the GUI
User exports a formatted Excel report
Teams reuse the report for benchmark communication
Technologies
Python for orchestration and parsing
Tkinter / ttk for the GUI
Regex for section extraction
openpyxl for Excel export

## Slide 19: IAR EWARM Map File Analyzer Technical architecture

## Slide 20: IAR EWARM Map File Analyzer Technical architecture

## Slide 21
Find out more at www.st.com

## Slide 22
For further support in creating a PowerPoint presentation, including graphic assets, formatting tools and additional information on the ST brand
you can visit the ST Brand Portal https://brandportal.st.com